Nec2 Short reference card

1		2	3	4	5	6	7	8	9	10	11
GW	Wire / geom	Tag / Nr	nr of / segs	X1	Y1	Z1	X2	Y2	Z2	wire radius
GM	Geom Move	Tag increm	new structs	Rot X (deg)	Rot X (deg)	Rot Z (deg)	Mov X	Mov Y	Mov Z	From Tag
GR	Geom Rotate	Tag increm	total structs
GE	no gnd	0		no ground plane present (Free Space)
	ground / plane	1		Ground plane present, wire-ends for Z=0 are ‘connected’ to ground / (GN card required; screen- and wire radius on GN card should be blank)
	ground	-1		Ground present, wire-ends are not ‘connected’ to ground (GN card required)
EX	Voltage / Src	0	tag nr	segm nr	XX ->	real volts	imag volts	(19: 0 No act.; 1 print rel.admit. matrix asymetry) / (20: 0 No act.; 1 print imp’s for frequency loop)
(*)	Current src	6	tag nr	segm nr	XX ->	real amps	imag amps

FR	linear	0	Nr of steps	0	0	start Mc	Step size			F1 = F0 + step
	log	1	nr of steps	0	0	start Mc	Step size			F1 = F0 * step
GN	free space	-1								Nullifies previous ground settings
	finite ground	0	nr rad. wires	0	0	diel. Const	Cond. S/m	radius screen	radius wires	(In meters) See also GE card / RP card must be set to 4
	perfect ground	1
	sommer / norton	2	0	0	0	diel. Const	Cond. S/m			note: conductivity must be negative for frequency loop
LD	nullify	-1
	serie RLC	0	tag nr	start segm	0/end segm	R ohms	L Henry	C Farad		LD card always in series with EX and TL cards
	parall	1	see 0			see 0				LD4 does not supno automatic frequency scaling
	serie RLC	2	see 0			R oh/m	L H/m	C F/m
	parall	3	see 0			see 2
	impe-dance	4	see 0			Resis. / Ohms	React. Ohms	-
	wire cond.	5	see 0			Cond. mho/m
(*)	LC trap	6	See 0			Q-coil	L henry	C farad
(*)	Insula-ted wire	7	See 0			Diel. const	Coat radius
TL	trans line	tag-nr port 1	seg-nr port1	tag-nr port 2	seg-nr port 2	imped ohms	Length mtrs	admit real 1	admit ima 1	admit real 2	admit ima 2
		a) Multiple ports are connected in parallel b) If connected to segment with LD; LD is in serie with TL
RP	normal	0	theta steps	phi steps	XNDA	theta start	Phi start	Theta stsize	phi stsize	far fld dist.	norm gain F
	add surf wave	1	see 0	XNDA: / 17: 0: major/minor axis; 1: vert/hor gain / 18: 0: no norm gain; 1-5: normalized gain / 19: 0: power gain; 1: directive gain / 20: 0: no avaraging; 1: avar gain; 2 avar gain						Add surface wave
	ground cond’s	2..3	see 0							Special ground conditions
	ground screen	4	see 0							Ground-screen; must be specified in GN card !
	gnd scr, cond’s	5..6	see 0							Botth ground-screen and special ground conditions
PQ	no charges	-1
	charges	0	tag nr	start segm	0/end segm
PT	all curr	-2
	no curr	-1
	Curr.	0	tag nr	start segm	0/end segm
	Receiv- pattern	1..3	tag nr	start segm	0/end segm					See page 74 manual

Geometry cards		I1	I2	F1	F2	F3	F4
		3-5	6-10	11-20	21-30	31-40	41-50
Prog-ctrl cards		I1	I2	I3	I4	F1	F2	F3	F4	F5	F6
		3-5	6-10	11-15	16-20	21-30	31-40	41-50	51-60	61-70	71-80