2nd midterm exam ANTENNAS AND PROPAGATION - 15.11.2016

1. Due to a design error a ground-plane antenna has the wrong radial length. Such an antenna has the following properties when compared to a correctly-designed GP antenna:

(A) lower radiation	(B) corrupted	(C) poor impedance	(D) all defects
efficiency	radiation pattern	matching	mentioned

2. A pyramidal horn is equipped with a WR90 waveguide flange intended for operation in the "X" band from 8.20GHz to 12.5GHz. What is the cutoff frequency of the fundamental waveguide mode fTE01=? with the internal dimensions 22.86mmX10.16mm? (c0=3•108m/s)

(A) 6.56GHz	(B) 8.20GHz	(C) 12.5GHz	(D) 13.1GHz

3. What is the directivity D=? of a reflector antenna with a diameter of d=3m intended for satellite reception at 4GHz. The reflector is illuminated by a corrugated horn that allows an illumination efficiency η=80%. (c0=3•108m/s)

(A) 39dBi	(B) 40dBi	(C) 41dBi	(D) 42dBi

4. A Yagi antenna uses a collimating lens made of artificial dielectric. The wave number k in the artificial dielectric εr>1 compares to the wave number k0 in free space in the following way:

(A) k=0	(B) k<k0	(C) k=k0	(D) k>k0

5. Which condition is NOT required to obtain a random electromagnetic field in a reverberation chamber with a Rayleigh distribution time dependance?

(A) one or more	(B) large enough	(C) at least four	(D) well closed
mode stirrers	wall reflection |Γ|≈1	antennas inside	chamber

6. A Huygens source has a radiation pattern F(Θ,Φ)=1+cosΘ. By how many a=? decibels the radiated electrical field strength decays in the direction Θ=π/4 and Φ=π/2 compared to the maximum radiation of the Huygens source?

(A) -0.7dB	(B) -1.4dB	(C) -2.1dB	(D) -2.8dB

7. A rotationally-symmetrical parabolic mirror has a depth of h=0.5m. The diameter of the mirror is equal to d=6m. What is the focal-to-diameter ratio f/d=? of the above-mentioned parabolic mirror?

(A) 0.188	(B) 0.375	(C) 0.75	(D) 1.50

8. The radiation pattern F(Θ,Φ) of a coherent antenna is measured in a free-space radio link at a sufficient distance (Fraunhofer) by rotating in a selected plane:

(A) just one of either	(B) both TX and RX	(C) always TX	(D) always RX
TX or RX antenna	antenna simultaneously	antenna only	antenna only

9. A TE02 mode propagates in a rectangular waveguide. The latter makes a smooth transition into a pyramidal horn. What is the aperture-illumination efficiency η=? in the direction z (propagation in the waveguide & horn), neglecting the phase error?

(A) 0%	(B) 50%	(C) 75%	(D) 82%

10. Different metal shapes can be used as the artificial dielectric of a Yagi antenna. In an antenna operating on both orthogonal polarizations the following shape can not be used:

(A) square loops	(B) rods in one plane	(C) right-angle crosses	(D) round disks

11. How many a=? decibels should the illumination decay at the edge of a rotationally-symmetrical parabolic mirror compared to its center to achieve the maximum antenna gain GMAX as a compromise between under illumination and spillover loss?

(A) -5dB	(B) -40dB	(C) -20dB	(D) -10dB

12. The Friis equation written in the form PRX=PTXGTXGRX(λ/4πr)2 can be used in the following cases of wireless communications:

(A) any TX	(B) coherent TX	(C) non-coherent TX	(D) any TX and
and any RX	and non-coherent RX	and any RX	coherent RX

Name:	Email: