5th midterm exam ANTENNAS AND PROPAGATION - 17.1.2017

1. The range of two handheld radios h1=h2=1.5m with omnidirectional antennas G1=G2=1 amounts to only d=3km. What is the receiver sensitivity PMIN=? if reflection from flat ground is suspected to be a limiting factor. The TX power amounts to P=1W at f=450MHz.

(A) -132dBm	(B) -102dBm	(C) -95dBm	(D) -65dBm

2. What is the radio range d=? from a h=30m tower above a flat country considering that due to refraction in the troposphere, the radio waves follow a curved line with a radius of R=25000km? The mean radius of the Earth is RZ=6378km.

(A) 9.8km	(B) 19.6km	(C) 22.7km	(D) 33.4km

3. A point-to-point radio link spans the distance r=10km. The first Fresnel ellipsoid is not obstructed. We are however limited with the antenna size dTX=dRX=30cm and atmospheric attenuation. Which frequency is the best choice for this link?

(A) 30GHz	(B) 300GHz	(C) 0.3GHz	(D) 3GHz

4. During daylight the plasma frequency of the ionosphere reaches fP=10MHz. At which frequency f=? the wavelength of radio waves in the ionosphere doubles when compared to the same wave in free space? (ε0=1/(4π•9•109)As/Vm, Qe=-1.6•10-19As, me=9.1•10-31kg)

(A) 7.1MHz	(B) 8.4MHz	(C) 13.3MHz	(D) 11.6MHz

5. At night the electron concentration Ne reaches its maximum at a height of h=300km in the ionospheric layer F. What is the maximum concentration Ne=?, if we measured MUF=12MHz? (ε0=1/(4π•9•109)As/Vm, Qe=-1.6•10-19As, me=9.1•10-31kg, RZ=6378km)

(A) 1.7•1011m-3	(B) 1.8•1012m-3	(C) 1.9•1013m-3	(D) 1.6•1010m-3

6. Fading measurement results are to be presented as a histogram. Choosing the number of columns we have to keep care about the following (circle the NONSENSE answer):

(A) too many columns	(B) there are no	(C) too few columns	(D) all results
increase noise	zero-height columns	reduce resolution	are represented

7. A broadside array is only required to operate over a narrow frequency band around f0 allowing a simple serial feed of its elements from a source on one side. At slightly higher frequencies f>f0 the radiation-pattern maximum moves in the following direction:

(A) towards source	(B) orthogonal to feed	(C) away from source	(D) doesn't move

8. A link margin, where the fading obeys the Rayleigh distribution, is designed for a probability of link loss of P=1%. What probability of link loss P'=? is expected in the case of a partial failure of the transmitter, its output power decreased by ΔPTX=-6dB?

(A) 0.7%	(B) 1.4%	(C) 2.0%	(D) 3.9%

9. A WiFi link with the antennas on the roofs of two distant buildings is disturbed by the reflection from the flat ground between the buildings. What kind of diversity is the most efficient in this case maximally reducing the link loss rate?

(A) frequency	(B) direction	(C) space	(D) time

10. Base stations of a mobile network should provide a useful range dU=2km and guarantee a minimum distance to the interferer (channel reuse) dM=12km. What it the minimum available signal-to-noise ratio S/N=? at a probability of link loss P=1%?

(A) 7dB	(B) 11dB	(C) 15dB	(D) 22dB

11. What transmitter power PTX=? is allowed to uniformly illuminate a d=1.8m parabolic mirror? Workers are located close to the antenna in the Fresnel region (parallel rays) and by applicable laws the electric field should not exceed EMAX=6Veff/m.

(A) 24dBm	(B) 27dBm	(C) 30dBm	(D) 33dBm

12. A pyramidal waveguide horn is equipped with a rectangular flange that has a rectangular aperture with the dimensions 15.8mm X 7.9mm. The described waveguide horn is an excellent antenna covering the whole frequency range:

(A) 4-6GHz	(B) 5-8GHz	(C) 8-13GHz	(D) 12-18GHz

Name:	Email: