2nd midterm exam HIGH-FREQUENCY TECHNOLOGY - 11.11.2016

1. The common electrode of a power RF transistor is connected to the heat-sink flange. An Ω-meter shows a rectifying junction from one of the other two electrodes and a low resistance R<1Ω from the other electrode towards the flange. The transistor is a:

(A) NPN common B	(B) power GaAs FET	(C) power LDMOS	(D) NPN common E

2. A high-frequency detector with a low-barrier Schottky diode U1mA=100mV is used to measure a RF power in the range P=+30dBm. What is the response of the detector U(P) where the power P is in Watts [W] and α is a proportional constant (with units):

(A) U=α.P	(B) U=α.P2	(C) U=α.√P	(D) U=α.P3/2

3. An unknown two-port network is described by the following S-parameter matrix: S11=0, S12=j, S21=-j and S22=0. The above network has the following electrical properties (circle the WRONG answer!):

(A) uncond.stable	(B) nonsymmetric	(C) nonreciprocal	(D) active

4. A coaxial cable with a polyethylene dielectric εr=2.25 has a characteristic impedance ZK=50Ω. At which shortest cable length l=? the load Z=(20+j0)Ω is transformed into a completely real impedance Z'=R'+j0 at a frequency f=100MHz? (c0≈3∙108m/s)

(A) 33.3cm	(B) 25cm	(C) 75cm	(D) 50cm

5. A bipolar-transistor amplifier is only conditionally stable because of CBK=CMILLER>0. Which countermeasure to achieve unconditional stability does NOT decrease the gain?

(A) resistive	(B) resistive	(C) neutralization in	(D) common base
feedback	output loading	a symmetric circuit	configuration

6. A large directional antenna is pointed to the Sun to achieve an antenna noise temperature TA=20000K. What noise power PN=? is available at the antenna connector, if the bandwidth of the antenna amounts to B=100MHz? (kB=1.38∙10-23J/K)

(A) -115.6dBm	(B) -105.6dBm	(C) -85.6dBm	(D) -75.6dBm

7. A low-noise preamplifier with a gain of G=15dB achieves a noise figure of F=0.5dB. What is the allowed noise figure FRX=? of the following receiver so that the noise figure of the whole chain does not exceed F'=1dB? (T0=290K)

(A) 3.5dB	(B) 7.3dB	(C) 6.4dB	(D) 15.5dB

8. A satellite receiving station includes an antenna with a gain of G=33dBi and antenna noise temperature of TA=40K. The antenna is connected to a receiver with a noise figure of F=0.8dB. What is the G/T=? figure of merit of this station? (T0=290K)

(A) 53dB/K	(B) 49dB/K	(C) 43dB/K	(D) 59dB/K

9. Direct-to-home satellite TV in the f=12GHz band was made possible by the availability of low-noise transistors. What kind of semiconductor allows the lowest noise performance in the f=12GHz frequency range?

(A) Si	(B) InP	(C) Ge	(D) GaAs

10. An antenna is first pointed in the cold sky with T1=10K and later into a ground black-body target (pine trees) at T2=290K. The power ratio is YdB=10log(P2/P1)=7dB. What is the total system noise temperature T=TA+TS=? while pointed in the sky?

(A) 10K	(B) 70K	(C) 150K	(D) 280K

11. The result of a noise temperature measurement deviates by ΔT=±30K around a center value of T≈400K due to the random nature of the measured signals. What is the expected deviation ΔT'=? if an average of N=36 successive measurements is used?

(A) ±5K	(B) ±11.11K	(C) ±0.833K	(D) ±30K

12. While measuring the noise figure of a high-gain receiver, some amplifier stages of the latter may be driven into saturation due to the random nature of the measured signals. In this case the obtained noise figure will result:

(A) too small	(B) too large	(C) equal to zero	(D) correct

Name:	Email: