4th midterm exam HIGH-FREQUENCY TECHNOLOGY - 23.12.2016

1. A LC circuit is oscillating at its resonant frequency f=10.7MHz. What is the Q=? of the circuit, if the average dissipated power equals to P=10mW corresponding to a voltage U=10Veff on the capacitor C=100pF?

(A) 135	(B) 17	(C) 33	(D) 67

2. A ladder band-pass includes series L1+C1 circuits in series branches and parallel circuits L2║C2 in parallel branches. In a narrow-band filter B<<f0 it is hard to make:

(A) series	(B) parallel	(C) series	(D) parallel
capacitor C1	capacitor C2	inductor L1	inductor L2

3. The performance of an oscillator is presented in a Rieke diagram. The following quantities are plotted in the Rieke diagram as a function of load matching Γ:

(A) frequency and	(B) frequency and	(C) stability and	(D) efficiency
output RF power	phase noise	output RF power	and phase noise

4. An interference at f=1GHz is attenuated by connecting a coaxial-cable stub in parallel to the receiver input using a T-adapter. What should be the stub length and how should the stub be terminated, if the cable uses a dielectric εr=2.25? (c0=3•108m/s)

(A) 2.5cm short	(B) 5cm open	(C) 10cm open	(B) 15cm Γ=0

5. An AT-cut quartz plate (v=3320m/s) is usually not made thinner than d<50μm, since even thinner plates break easily. If the crystal is marked f=108.15MHz on the package, this frequency most likely represents the following mechanical mode of oscillation:

(A) 3rd overtone	(B) fundamental mode	(C) 7th overtone	(D) 5th overtone

6. Which modes of oscillation of a quartz crystal do not couple mechanical energy in the surrounding air and therefore do not require a vacuum envelope for the highest Q?

(A) pressure	(B) shear	(C) any bulk	(D) tuning-fork
modes	modes	modes	modes

7. An AT-cut quartz plate with a thickness d=100μm and diameter 2r=8mm has 2D and 3D resonances just slightly above the 1D-fundamental-mode frequency. The unwanted 2D and 3D resonances can be suppressed by the following property of the plated electrodes:

(A) shape	(B) thickness	(C) conductivity	(D) roughness

8. A mechanical resonator made of piezoelectric ceramic (piezoelectric coupling) has the following electro-mechanical properties when compared to a quartz crystal:

(A) higher Q and	(B) higher Q and	(C) lower Q and	(D) lower Q and
weaker coupling	stronger coupling	stronger coupling	weaker coupling

9. A microprocessor uses a crystal oscillator at f=20MHz as its clock source. The resonator achieves a QL=5000 in the oscillator circuit. What is a sensible choice for the time constant τ=RC determining the microprocessor RESET delay?

(A) 1μs	(B) 100μs	(C) 10ms	(D) 1s

10. A LC (QL=30) oscillator for f=100MHz employs a silicon NPN transistor with a RF noise figure of F=3dB. The bias circuit is carefully design to avoid degrading the phase noise. At a frequency offset of Δf=100kHz the phase noise is proportional to:

(A) L(Δf)=α.f-3	(B) L(Δf)=α.f-2	(C) L(Δf)=α.f-1	(D) L(Δf)=konst.

11. The signals of two similar oscillators at f1=3.0GHz and f2=3.1GHz are mixed to obtain the difference f2-f1=100MHz. What is the difference phase noise L'(Δf)=? at an offset Δf=100kHz, if each oscillator alone has L(Δf)=-90dBc/Hz at the same offset?

(A) -87dBc/Hz	(B) -90dBc/Hz	(C) -93dBc/Hz	(D) -84dBc/Hz

12. A semiconductor noise source includes a PN-junction silicon diode using the avalanche breakdown. At what reverse voltage the avalanche diode produces the largest amount of radio-frequency noise?

(A) 0.7V	(B) 2V	(C) 6V	(D) 18V

Name:	Email: