NOISE IN RADIO COMMUNICATIONS - QUIZ - 5.2.2017

1. At which frequency f=? the shot-noise spectral power density equals the Rayleigh-Jeans approximation for thermal noise? The temperature of all equipment used is equal to T=20°C. (h=6.626∙10-34Js, kB=1.38∙10-23J/K, c=3∙108m/s)

(A) 22GHz	(B) 510GHz	(C) 6.1THz	(D) 231THz

2. What noise power PN=? is available at the connector of a lossless antenna pointed to a black-body (Γ=0) target at T=2000K? The antenna operates at a center frequency of f0=10GHz, its bandwidth equal to Δf=10%f0. (kB=1.38∙10-23J/K)

(A) 28pW	(B) 4.0pW	(C) 1.4∙10-14W	(D) 2.8∙10-20W

3. What is the noise temperature TA=? of a lossless antenna with a directivity of D=30dBi pointed to the Sun? The Sun has an angular diameter of αS=0.5° and radiates as a black body at TS=106K. The cold-sky background is at TN=10K.

(A) 486K	(B) 4770K	(C) 10K	(D) 106K

4. A monolithic IC manufacturing process allows transistors with a gain of G=7dB and noise temperature of T=400K at room temperature at a frequency f=50GHz. What noise temperature TRX=? can achieve a receiver built in the above-mentioned technology?

(A) 200K	(B) 300K	(C) 400K	(D) 500K

5. What is the G/T figure of merit of a satellite ground station with a lossless antenna temperature of TA=25K and a receiver with a noise figure of F=0.5dB? The antenna gain is equal to G=40dBi. (T0=290K)

(A) 2.2dB/K	(B) 22.2dB/K	(C) 37.8dB/K	(D) 57.8dB/K

6. A low-noise front end has to be designed for a K-band satellite receiver operating at f=20GHz. Which of the following device technologies is best suited for the low-noise front end?

(A) N-channel MOSFET	(B) Si PNP	(C) GaAlAs HEMT	(D) SiGe HBT

7. A hot/cold ratio Y=3dB is obtained while measuring an unknown high-gain amplifier with a noise head having the hot temperature T2=1000K and cold temperature T1=T0=290K equal to room temperature. What is the noise temperature T=? of the amplifier?

(A) 420K	(B) 65K	(C) 1000K	(D) 290K

8. What is the required signal-to-noise ratio S/N=? in a radio link using BPSK modulation to obtain a BER=10-9? The real-world demodulator loss amounts to a=2dB when compared to an ideal BPSK demodulator.

(A) -1.6dB	(B) 10.6dB	(C) 12.6dB	(D) 14.6dB

9. The local oscillator of a satellite TV receiver operates at fLO=10.5GHz and includes a Q=1000 dielectric resonator coupled to an active device. Which of the following semiconductor devices is best suited for this purpose?

(A) GaAlAs HEMT	(B) avalanche diode	(C) N-channel MOSFET	(D) Si NPN

10. An oscillator for f0=20MHz uses a LC circuit with a QL=30. What improvement of the oscillator phase noise L(Δf) is expected at an offset of Δf=300Hz when the LC circuit is replaced with a quartz crystal wit a QL=3000?

(A) 40dB	(B) 30dB	(C) 20dB	(D) 10dB

11. A simple LC oscillator (QL=10) for f0=300GHz is built as a technology demonstrator for a SiGe process with a noise figure of F=10dB. What spectral-line width fFWHM=? is expected at an operating power of P0=-10dBm? (kB=1.38∙10-23J/K, T0=290K)

(A) 28MHz	(B) 280kHz	(C) 2.8kHz	(D) 28Hz

12. A binary shift register includes m=17 D-flip-flops connected into a chain. The maximum sequence length that can be produced by a linear feedback network including only EXOR gates is equal to N=?

(A) 65535	(B) 65536	(C) 131071	(D) 131072

Name:	Email: